REC Register Description
ADDRESS	BITS	FUNCTION
$DF00 / 57088	7-0	Status Register – Read Only / 7 – Interrupt Pending 1 = Interrupt waiting to be serviced / 6 – End of Block 1 = Transfer complete / 5 – Fault 1 = Block verify error / 4 – Size 0 = Total expansion = 128K / 1 = Total expansion = 512K / 3-0 – Version / Note: Bits 7-5 are cleared when this register is read
$DF01 / 57089	7-0	Command Register – Read/Write / 7 – Execute 1 = Transfer per current config / 6 – Reserved / 5 – Load 1 = Enable AUTOLOAD option / 4 – FF00 1 = Disable FF00 decode / 3 – Reserved / 2 – Reserved / 1,0 – Transfer type: 00 = transfer from C64 to RAM module / 01 = transfer from RAM module to C64 / 10 = swap between C64 and RAM module / 11 = verify C64 and RAM module
$DF02 / 57090	7-0	C64 Base Address, LSB – Read/Write / Lower 8 bits of base address
$DF03 / 57091	7-0	C64 Base Address, MSB – Read/Write / Upper 8 bits of base address
$DF04 / 57092	7-0	RAM module address, LSB – Read/Write / Lower 8 bits of base address
$DF05 / 57093	7-0	RAM module address, MSB – Read/Write / Upper 8 bits of base address
$DF06 / 57094	2-0	RAM module bank – Read/Write / RAM module bank pointer / Bits 2 (MSB) to 0 (LSB) are significant
$DF07 / 57095	7-0	Transfer length, LSB – Read/Write / Lower 8 bits of the byte counter
$DF08 / 57096	7-0	Transfer length, MSB – Read/Write / Upper 8 bits of the byte counter
$DF09 / 57097	7-5	Interrupt Mask Register – Read/Write / 7 – Interrupt enable 1 = Interrupt enabled / 6 – End of Block mask 1 = Interrupt on end of block / 5 – Verify error 1 = Interrupt on verify error
$DF0A / 57098	7-6	Address Control Register – Read/Write / 00 = Increment both addresses (default) / 01 = Fix expansion addresses / 10 = Fix C64 addresses / 11 = Fix both addresses